## Slide 1: Team 18 - Part 2
Mechanical Design and Transmission Components

## Slide 2: Team 18 Members: Md Sepehr Rezvanifard Harsimranjeet Karamvir
Proposed Vehicle:
Light and quick electric vehicle
Single Passenger
Intended for short trips in the city
Low Maintenance
High Safety considerations

## Slide 3: Chassis: Tadpole Configuration -More stable than delta for 3 wheel vehicles Space Frame Design -Constrained trusses that withstand bending stress
Chassis Structural Members:
-Pipe Cross Section
-ISO Standard
-(26.9 x 3.2)mm
-SAE 1060 Plain Carbon Steel

## Slide 5: Drive Train High Level
Emrax 208 Electric AC Synchronous Motor
Motor RPM - 3000RPM
Motor Torque - 163Nm (120ftlb)
Wheel Diameter - 15”
Wheel RPM(Max) - 1344
Max Speed - 60mph

## Slide 6: Drivetrain Exploded View

## Slide 7: Belt Drive System
Specifications:
-Baldor 5V Belts -Output RPM (Driving Belt): 2280RPm
-Diameter (Sheaves) - 7.10” and 10.9”

## Slide 8: Belt Selection from an industrial manufacturer

## Slide 9: Gear Drive Subsystem
Diameter of pinion (Driving Gear): 3 inches
Number of teeth: 18
Diameter of Idler gear: 8 inches
Number of teeth: 48
Diameter of Driving Gear: 27
Idler gear was used to increase the the center distance
Required RPM to the shaft : 1400 RPM
Theoretical output: 1386 rpm

## Slide 10: FEA Analysis (In Progress)
Crash Stress Analysis for 100Kg Payload and max speed of 60mph - 144KN Distributed load

## Slide 11: Safety - Inertial Measurement Unit Sensor -Good Battery Management System - Aggressive Safety Factors, when designing belt and gears - Two grounds to isolate high voltage and low voltage components - Electric vehicle controllers offer more control on motor rotation and speed than internal combustion engine
Cost
Motor - $4500 CAD
Structural Members (1060 Plain Carbon Steel) - $800
Battery (18650s) - $3000
Competitors Price (Electra Mechanical Solo) - $20500